## Slide 1: A robot that swims in grain silos

## Slide 2
part 1
Solid or fluid?

## Slide 3
Dust
Soil
Foodstuff
Water
Paint
One equation
Many equations
A mathematical model is needed!

## Slide 4: Dry granular systems
  Gravity
  Contact force
Notes: Dry systems form piles, flow.
Effectively there's no fluid in between.
Only two forces, really.
Gravity is easy to simulate. We'll come back to contact forces soon.

## Slide 5: Grain silos are tough work
  Temperature, moisture, infection: vital to monitor

## Slide 6: Robots!
Mole Crab
CRABOT
Paramecium
CRABOT 2
Notes: CRABOT: Paddle-like motion
Sandfish: Undulating (up and down) motion

## Slide 7: Robots!
Mars Underground Mole
Notes: Mars Mole uses internal hammer
Only a few cm depth reached for all robots
InSight mission most successful
  Underestimated Mars' soil density
  Had to thwack the robot down with the rover's arm

## Slide 8: Robots!
Sandfish
Undulating robot
A robot that swims in grain silos
Notes: CRABOT: Paddle-like motion
Sandfish: Undulating (up and down) motion

## Slide 9: The "Crover"
Fin (for stability)
Two hemispheres – may move independently
Ridges (push against grains)
Sensors
Notes: We want to see how this performs against the mu(I) rheology model

## Slide 10
The Conti Model
part 2

## Slide 11: Parameter space
Notes: As I'm sure you can tell, this simple model has a lot of dials we can play with. For example, we could take D, the diameter of the robot relative to grains, and omega, how fast the robot turns. The aim of this study is to essentially tweak these dials until we arrive at an optimal solution. We know that a robot may be able to change its motor intensity, for example, but it can't change its size.
What we want to do is embed this onto "parameter space", treating each parameter as a different dimension. That way we can easily measure things – for example, see here how each tiny cross is a simulation, giving us a patchwork of information.
Actually, we explored three dimensions – just under 8,000 simulations, in various different slices, also checking how friction affects movement. The model originally meant to be able to dynamically change its friction by extending fins, but this proved to break far too often.
Actually, this is more than a 3-parameter space – in reality, there are at least 16 dials to turn. But to avoid going slightly crazy, we'll stick with these three.

## Slide 12: Conti simulation
z
Robot
Grain
Pressure gradient
crystal diagram
Notes: So now let's generate some objects to put forces on. This diagram is taken directly from Lorenzo's paper.
Many particles: a robot as a "stick".
Grains vary in size – this avoids them 'crystallising' into . We found variation of 20% from the mean was "good enough".
Also note that the side boundary is periodic – this lets us save space while avoiding the effect of being near a wall.
Due to gravity, there is a pressure gradient – grains on the bottom have the weight of all those above them. This is what rotation exploits: at higher pressures, we have a slightly greater friction. If you've ever heard of the Magnus effect, there is sort of a similar thing going on here, but we won't focus on it too much.

## Slide 13: Noether's theorem
Symmetry ↔ Conservation
e.g. Space-time ↔ Momentum-energy
Fundamental and essential
Can 2D simulations use this?
Emmy Noether, 1882—1935
z
Notes: Emmy Noether is my fave – seriously, I named my favourite software package noether after her. In addition to her redefinition of several fields of mathematics, she briefly did a little bit of physics, and just so happened to write a groundbreaking physical theorem: symmetry and conservation are two sides of the same coin.
For example. The laws of physics don't change if we move around — with Noether's theorem, this means momentum is conserved. Likewise, the laws of physics don't change over time – so energy is conserved.
This is a really beautiful theorem – it says so much about the universe, and also gives us some rather useful hints, having helped quantum physicists wrangle new and weirder symmetries and conservations.
The robot will rotate in the xy axis, and the PhD paper shows there are zero z-axis forces. On average, therefore, there is a z-axis symmetry – so on average, we may get some results from 2D, right? This will make simulation far more efficient — and even with a supercomputer, we need everything we can get.

## Slide 14
Coding it up
part 3

## Slide 15: Exploring parameter space
0
1
Linear
}
Defined step
Notes: Speaking of bizarre glitches. Let's talk about one so strange I got new physics out of it.
So you can see here a time series of the force. It starts off noisy but consistently, and then — static.
I managed to capture this right as it happens, and as you can see, there are separate oscillations normal and tangential to the force.
Physically, this looks like all the particles are static, which is definitively not expected behaviour. It's sort of equivalent to if suddenly particles started acting like gears — they're all turning against one another and staying in the same place, bouncing back and forth and only spinning.
Now we can start to avoid this by introducing a standard bumpiness. However, this only keeps slippage at bay – and makes calculating friction coefficient more involved, of course.

## Slide 16: Exploring parameter space
0
1
1/2
3/4
1/4
1/8
3/8
5/8
7/8
Bifurcation
Notes: Speaking of bizarre glitches. Let's talk about one so strange I got new physics out of it.
So you can see here a time series of the force. It starts off noisy but consistently, and then — static.
I managed to capture this right as it happens, and as you can see, there are separate oscillations normal and tangential to the force.
Physically, this looks like all the particles are static, which is definitively not expected behaviour. It's sort of equivalent to if suddenly particles started acting like gears — they're all turning against one another and staying in the same place, bouncing back and forth and only spinning.
Now we can start to avoid this by introducing a standard bumpiness. However, this only keeps slippage at bay – and makes calculating friction coefficient more involved, of course.

## Slide 17: Curious glitch when implementing 2D sim
z
Notes: Speaking of bizarre glitches. Let's talk about one so strange I got new physics out of it.
So you can see here a time series of the force. It starts off noisy but consistently, and then — static.
I managed to capture this right as it happens, and as you can see, there are separate oscillations normal and tangential to the force.
Physically, this looks like all the particles are static, which is definitively not expected behaviour. It's sort of equivalent to if suddenly particles started acting like gears — they're all turning against one another and staying in the same place, bouncing back and forth and only spinning.
Now we can start to avoid this by introducing a standard bumpiness. However, this only keeps slippage at bay – and makes calculating friction coefficient more involved, of course.

## Slide 18
Nice!
WHAT
Notes: Speaking of bizarre glitches. Let's talk about one so strange I got new physics out of it.
So you can see here a time series of the force. It starts off noisy but consistently, and then — static.
I managed to capture this right as it happens, and as you can see, there are separate oscillations normal and tangential to the force.
Physically, this looks like all the particles are static, which is definitively not expected behaviour. It's sort of equivalent to if suddenly particles started acting like gears — they're all turning against one another and staying in the same place, bouncing back and forth and only spinning.
Now we can start to avoid this by introducing a standard bumpiness. However, this only keeps slippage at bay – and makes calculating friction coefficient more involved, of course.

## Slide 19: Slippage
μ?
Notes: Speaking of bizarre glitches. Let's talk about one so strange I got new physics out of it.
So you can see here a time series of the force. It starts off noisy but consistently, and then — static.
I managed to capture this right as it happens, and as you can see, there are separate oscillations normal and tangential to the force.
Physically, this looks like all the particles are static, which is definitively not expected behaviour. It's sort of equivalent to if suddenly particles started acting like gears — they're all turning against one another and staying in the same place, bouncing back and forth and only spinning.
Now we can start to avoid this by introducing a standard bumpiness. However, this only keeps slippage at bay – and makes calculating friction coefficient more involved, of course.

## Slide 20
Ness and Cates
Notes: As it turns out slippage is inevitable for everything.
…but the parameters significantly affect the probability.
  On the left we have time without slippage – yellow means better. On the right we have some variable that is nearly exactly aligned to the probability of slippage – after some threshold, slippage never occurs!
Ness and Cates did a study on a toy model with two parameters – some "delta" for the force, and packing fraction.
  In it they find a "dynamic" region and two "absorbing regions", with a distinct phase transition between them.
  "Absorbing region 2" has low, near-zero activity. It nearly perfectly matches slippage.
  "Absorbing region 1" meanwhile has utterly no activity. Indeed, toying around with gravity, I recreated this exactly.
  I came up with a hypothesis that this applies to every simulation of systems — in which the phase parameters are the packing fraction and the shear force.

## Slide 21
Saving Grains
part 4

## Slide 22: 391,000,000 kg/day to storage loss
UN Food. Agri. fao.org/3/mb060e/mb060e00.pdf
This many grains just got lost in this presentation
Notes: So, for context: grain is rather important. In this United Nations study – blame them for dividing the countries so weirdly – about 6 percent of food production is lost worldwide entirely because of poor storage quality. But that doesn't mean we can safely keep wasting food — a comparable amount is wasted by us simply binning food we don't eat.
One way we can avoid both problems is by monitoring grain quality. A robot that can move around a grain silo is super useful, as it can not only keep infection at bay efficiently, but also look out for conditions that might mean picky supermarkets would throw it out anyway. Being able to navigate right into the heart of a grain silo is super important.

## Slide 23: Cute robots!

## Slide 24
3D
2D

## Slide 25: Thank you!
"Two-dimensional approximation of rotational locomotion in a dry granular system"